# Description
## System
WIDGETLORDS Multipurpose I/O (WL-MIO) process controller is an open, space efficient DIN mounted industrial process controller solution that provides reliable, flexible, maintainable, and scalable product that supports electronic components and software modules to change over time without changing I/O device wiring. WL-MIO process Controller lands I/O device wiring “one last time”!

### Open Industrial Process Controller Solution
Paramount to WL-MIO’s design approach is maximizing open standard’s based interfaces. Where standards do not exist, WL-MIO publishes specifications to support an open interface that extends the product life indefinitely and provides for the market to provide innovative solutions to enhance product function. WL-MIO’s open and standard’s based interface specifications are available for:
Interface to device wiring
Mechanical I/O modules dimensions
Electrical bus and connector pin definitions and connector part numbers
I/O module inter-process communications
Processor compute module
Power distribution
Software programming application programming interface
Python
C (enables Node Red, IEC-61499, IEC-61131)
Publishing these interface specifications enables flexibility to enhance function and maintainability over a longer time period.

### Basic Components
WL-MIO process controller consists of these four basic components:
Backplane. {hyperlink to Backplane description}
Processor and I/O module bus power supply (optional) {hyperlink to Power Supply 5 VDC Module description}
Processor module {hyperlink to Processor Modules description}
I/O Modules
The WL-MIO I/O modules offered are:
#### Analog Input SDAFE mA & VDC Module 4 Channel {hyperlink to description}
Analog Input Thermistor NTC 10K Ω Module 8 Channel {hyperlink to description}
Analog Output 0-20 mA Module 4 Channel {hyperlink to description}
Digital Input Discrete, Frequency, & Pulse Module 4 Channel {hyperlink to description}
Relay Output 2 A SPDT Module 4 Channel {hyperlink to description}
(The text hyperlink references additional information about each WL-MIO component.)
Package size of WL-MIO is 8.25 in. H x 5.8 in. W x 3.5 in D. DIN rail length consumed is 8.25 in. Depending on WL-MIO unit configuration, a minimum of 32 I/O devices are supported. That is a density of 3.9 I/O per DIN rail inch!

### Flexible and Scalable for product growth and longevity.

The following three configurations illustrate WL-MIO’s flexibility and hardware scalability capabilities for solutioning small to large control systems.

		Backplane Unit Quantity
Configuration	Basic WL-MIO Components	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16
Internal Processor and Bus Power Supply with mix of all WL-MIO I/O modules	Processor and Bus Power Supply	1		1		1		1		1		1		1		1
	Processor Module	1
	I/O Modules (4 I/O devices minimum)	6	8	7	8	7	8	7	8	7	8	7	8	7	8	7	7
	Total Backplane Slots Used	8	8	8	8	8	8	8	8	8	8	8	8	8	8	8	7
	Cumulative I/O Devices (minimum)	24	56	84	116	144	176	204	236	264	296	324	356	384	416	444	472

External Processor and Bus Power Supply with mix of all WL-MIO I/O modules	Processor and Bus Power Supply
	Processor Module	1
	I/O Modules (4 I/O devices minimum)	7	8	8	8	8	8	8	8	8	8	8	8	8	8	8	7
	Total Backplane Slots Used	8	8	8	8	8	8	8	8	8	8	8	8	8	8	8	7
	Cumulative I/O Devices	28	60	92	124	156	188	220	252	284	316	348	380	412	444	476	504

Internal Processor and Bus Power Supply with selected WL-MIO I/O modules (excludes Relay Output Module)	Processor and Bus Power Supply	1			1			1			1			1			1
	Processor Module	1
	I/O Modules (4 I/O devices minimum)	6	8	8	7	8	8	7	8	8	7	8	8	7	8	8	6
	Total Backplane Slots Used	8	8	8	8	8	8	8	8	8	8	8	8	8	8	8	7
	Cumulative I/O Devices (minimum)	24	56	88	116	148	180	208	240	272	300	332	364	392	424	456	480

Up to eight WL-MIO I/O modules may positioned in any backplane position to accommodate existing I/O device wiring and / or implementation specific design considerations. Distance between backplane units may be located up to XX feet apart to accommodate distributed I/O device termination locations being controlled by one WL-MIO solution.

### Continuity of Operations
To achieve implementation specific continuity of operations, the WL-MIO solution supports redundant modules for bus power and processor for one or more WL-MIO units.

### Maintenance
Access to I/O device terminal blocks and enclosure fasteners is from top surface of the WL-MIO unit. To add or replace I/O modules, four enclosure screw are removed and the backplane unit’s cover lifts off.

Each WL-MIO module is designed for “hot-swap”. Therefore, the entire system does not require power-down to insert new modules or replace failed modules. Additional backplane units may added to an existing solutions without powering down.

Backplane I/O positions are do not permit an I/O module to be inserted incorrectly. I/O module installation provides a positive feedback to the installer when performed correctly.

Color coded terminal blocks are coordinated with the backplane I/O position to facilitate ease of I/O device wiring or troubleshooting. Each color coded terminal block contains a numeric label that is mapped to each specific WL-MIO I/O module.

When additional technical information is required in the field, each I/O, Processor, Power Supply, and Backplane field replaceable unit contains a QR code that links to associated technical information specific to the field replaceable unit.